support@ipitomy.com | 941.306.2200

________________________________________________________________

Configuration of Valcom VIP-201 Paging Gateway

This document will inform the IPitomy Technician on the configuration and installation of the Valcom VIP-201 SIP based paging Gateway.

The Valcom VIP-201 SIP based paging Gateway is designed for use with virtually all IP based telephone systems. This guide will step you through configuration to IPitomy PBX products. The Unit provides 8 SIP addressable groups, and 1 Analog I/O. The VIP -201 can control thousands of IP and/or analog speakers or provide an interface to legacy based Paging systems.

The first step in setup is to create an Extension in the PBX for the VIP to use. Simply navigate to Destinations and then Extensions within the PBX and manually create one extension. Make note of both the Extension number and the Extension SIP password as this is required to be populated within the VIP for it to register. The device type for your Extension should be generic.

You must install the Valcom Configuration utility to configure the Valcom. This is provided on a CD that is included within the package for the VIP. Once installed the software will search your network for connected Valcom devices.

The software displays to you a list of the connected devices it finds. Select the VIP from the list and you can then configure it.

You will need to configure the Network settings first. You may use either a static assignment or dynamic. IPitomy generally recommends dynamic assignments be used.

You should then configure the SIP settings. This will include the IP of the IPitomy PBX for the SIP server field and the Phone number and Authentication fields and the SIP password is used in the Secret field. The rest of the page may be left at its defaults.

You should then configure the Channels page. All that is necessary is to make certain that the dial code is the extension as well. Once complete ou should update the device from the communications screen so that it is set with the values you have installed.

You can then connect the analog paging and SIP paging devices to the unit. Paging is accomplished via a call placed to this station.